The  Ultimate  Wi-Fi  Antenna

" Catch  Far  Away  Wireless  Signals "

All You Need is a Spare USB Port for them to Work    That's it !

Instantly improving your computer's WiFi   Reception !

1st  What’s Out There ?

Numerous antennas out there are good for 800ft, 1200ft, 1800ft range and selling @ $99 to $189

If you have a newer computer with Built In Wi-Fi you can not plug most others in.   So then you have to buy a wi-fi card and adaptor to hook them up.   (= approx. $300 investment)

These Antennas - can be good for Miles!    Yes Miles !     for  Le$$

##### (Just plug into your USB)

trek-america@pocketmail.com

www.discount-rv-marine.com

VoiceMail   303 - 358 – 8539

| Frequency: | 2400-2500 MHz |
| --- | --- |
| RF Power: | +30dBm |
| HP Beam Width: | Approx. 56 deg. |
| Impedance: | 50 Ohm |
| VSWR: | <1.5:1 avg. |
| Standard: | IEEE-802.11 a/b/g/n |
| Bus Type: | USB2.0 Type A |
| Modulation: | OFDM with BPSK, QPSK, 16QAM, 64QAM (11g), BPSK, QPSK, CCK (11b) |
| Radio Technology: | Direct Sequence Spread Spectrum (DSSS) |
| Data Rate: | 300/150/108/54/48/36/24/18/12/11/9/6/5.5/2/1Mbps auto fallback |
| Security: | 64/128/256-bit WEP Encryption, WPA/PSK,WPA2/PSK(TKIP, IEEE 802.1x) + AES |
| Drivers | Windows 98SE, 2000, Vista, ME, XP, Windows7, MAC + Linux |
| LEDs | Link, Activity |
| Temperature | 32~122°F (0 ~50°C) |
| Humidity: | 0~95% (Non Condensing) |
| Length: | 12" |
| Material Base: | Metal (Aluminum) |
| USB Cable: | Optional 5 meter Included (standard is 3 meters) |

How it Works !!  You don't need to buy expensive Type N or  Pigtail Cables, Adaptors + Wifi Card to make it work.     This is a Complete plug and play system.  Just plug your Antenna into your PC or Laptop via the USB Cable. The Built-In WiFi Card on the antenna is connected directly to your PC like a Wifi Card inside your computer, this mean you get 100% of the signal.

Coax  or  USB   With Coax you get

an analogic signal from the antenna to a

computer and you lose signal quality at

every foot, every adaptor, connector

etc.    With USB you get a numeric signal

already analyzed by the Wifi  Device, so

you don't lose dbm    (signal strength)

Customer Comments -    One day in a

store Parking lot, I turned on my laptop and got 3

signals. (one strong enough) after hooking up the

antenna and placing it on the bed inside the RV and

turning it I found 29!!

At our campground site we always had to go down

to the office to connect.  Now we can set in our RV

and download the pictures that we get of our

Grandchildren.         Thanks !!

Our Son lives 5 blocks away (thru buildings) he has

now cancelled  his internet service and uses our

Wireless. an Amazing Product!

At an RV Rally I had 4 signals, I purchased your

antenna, and Wow!  26 Signals !!!